## Slide 1
494(P)-NAV-01: Basic Navigation
Ashilta
Trainee Preparation
01 Oct 2020
01 Apr 2020

## Slide 2: Lesson Overview
Rules of the Air
Navigation Principles
Basic Altimetry
Dead Reckoning/VFR Navigation
Instrument Flight
494(P)-NAV-01

## Slide 3: Rules of the Air
Understanding Rules of the Air
Common Speed Restrictions
Understanding Aircraft Lighting
494(P)-NAV-01

## Slide 4: Understanding Rules of the Air
Rules of the Air exist to ensure that all users of airspace are able to operate safely in the proximity of each other, particularly where no control service is available to support separation.
Given that military jets are typically of significantly higher performance than civilian jets, having a simple framework in place greatly enhances safety.
For the purposes of our simulation, the ‘Rules of the Air’ do not consist of the plethora of texts in reality. Instead, a simpler set of much simpler to understand rules are used in order to ensure safety whilst not encumbering pilots.
494(P)-NAV-01

## Slide 5: Understanding Rules of the Air
Typically, aircraft in the air have priority over those on the ground; for example, a landing aircraft should have priority over a departing aircraft.
When airborne, aircraft already on the right have right of way. For example, an aircraft joining the circuit with traffic to their right should give way to that traffic.
Traffic experiencing emergency situations should always have priority over others. This includes scrambling aircraft.
When flying, follow the mantra ‘Aviate, Navigate, Communicate’. Flying the aircraft safely is the highest priority, followed by being in the right place. Communicating with others is the lowest priority.
494(P)-NAV-01

## Slide 6: Common Speed Restrictions
Most military performance are high performance aircraft and, in reality, are typically exempt from the Rules of the Air. However, in order to maximise safety, a number of common speed restrictions are recognised and should be adopted where practicable.
Below FL250, civilian aircraft will not exceed 250 knots.
When operating within an aerodrome traffic circuit, patterns should not be flown in excess of 200 knots.
When commencing an approach the aircraft speed should not exceed 200 knots. Ideally, aircraft should be ‘on speed’ from the beginning of the approach unless otherwise instructed by ATC.
494(P)-NAV-01

## Slide 7: Understanding Aircraft Lighting
Modern aircraft are equipped with a variety of lights to ensure that they are visible in low light or low visibility conditions.
Most aircraft have a flashing strobe, typically mounted on the highest part of the aircraft. The strobe flashes white when activated. The flash may be a single flash or a series of short pulses.
Most aircraft also have navigation or position lights mounted in the wingtip – one wing light is green, the other is red. On all aircraft featuring these lights, the red light is on the left wingtip, allowing pilots to easily identify the aspect of other aircraft.
Aircraft will typically have a landing light, mounted in the nose gear.
The proper operation of lights on aircraft is critical. Lighting procedures can be found in the 132nd Multiplayer Instructions document.
494(P)-NAV-01

## Slide 8: Navigation Principles
Understanding Flight Rules
Navigation Methods
Understanding Heading vs Track
494(P)-NAV-01

## Slide 9: Understanding Flight Rules
Aircraft typically fly by one of two flight rules, called Visual Flight Rules (VFR) or Instrument Flight Rules (IFR). Other flight rules are available but are not relevant to the 132nd Virtual Wing.
Visual Flight Rules typically involve pilots navigating predominantly by reference to the view outside their window.
Instrument Flight Rules involve using a series of radio navigation aids, GPS systems or other instruments to navigate safely.
Whilst airborne, it’s possible to change the flight ruling that a flight operates under. For example, a flight may depart an airfield visually but later encounter bad weather, subsequently flying under IFR.
494(P)-NAV-01

## Slide 10: Navigation Methods
For flights within the 132nd, it is likely that both VFR and IFR will be used in the same flight.
Many flights in the vicinity of an aerodrome, in good weather, operate under VFR using ‘Dead Reckoning’ navigation.
Dead Reckoning navigation relies on a pilot identifying landmarks, points of interest or pre-determined objects as points of reference to navigate by.
This form of navigation relies on unchangeable visual references to navigate by. For example, roads, rivers and railways are good examples of landmarks which do not change rapidly and are more easily identifiable from the air.
494(P)-NAV-01

## Slide 11: Navigation Methods
Missions flown in the F/A-18C Hornet are likely to make use of Waypoints/Steerpoints, which are navigated to using an INS system on board the aircraft.
Navigation can also be undertaken using TACAN – a form of navigation aid adopted by the military, relying on a radio transmitter and receiver working together to provide lateral guidance. By detecting specific phases of the radio waves in use, a TACAN can be flown to on a specific bearing or ‘radial’.
ADF systems – Automatic Direction Finder – can be used to navigate to a Non-Directional Beacon or NDB. NDBs can be ‘tracked’ on a similar basis to TACAN or VOR, but only provides a direct bearing from the ADF to the beacon.
494(P)-NAV-01

## Slide 12: Understanding Heading vs Track
When performing certain navigation tasks, such as tracking a specific radial to a beacon or performing certain approaches, it is important to compensate for the effect of wind on the aircraft.
In normal circumstances, winds blow faster at higher altitudes. Subsequently, if an aircraft is subject to a crosswind, they are likely to be blown off track.
When flying a heading, the effect of wind is not accommodated for. Subsequently, the track will be different from the heading
To fly a track, the aircraft must fly a heading into the wind in order to nullify the effect of the wind pushing the aircraft.
494(P)-NAV-01

## Slide 13: Basic Altimetry
How Altimeters Work
Altitudes, Heights and Flight Levels
Navigation and Vertical Separation
494(P)-NAV-01

## Slide 14: How Altimeters Work
The higher into the atmosphere something moves, the less dense the air is. Through the relationship between density and pressure, this reduction in density also leads to a reduction in pressure.
A conventional altimeter works by measuring the difference between a ‘reference’ pressure setting and the pressure that an airframe is experiencing due to it’s distance above the earths surface.
In the first altimeters, a series of plates or ‘wafers’ are subject to a calibrated, pressured environment. As the ambient pressure increases or decreases, the distance between the plates increases or decreases accordingly. As the plates move further apart, the needles on the altimeter increase, indicating an increase in altitude.
494(P)-NAV-01

## Slide 15: How Altimeters Work
Due to the variations in localised pressure across the earth, altimeters must be regularly adjusted to ensure that the correct relationship between the calibrated pressure and ambient pressure.
In digital altimeters, a similar process is followed but without the mechanical diaphragm which interacts with the wafers and needles in an older altimeter.
494(P)-NAV-01

## Slide 16: Altitudes, Heights and Flight Levels
The term ‘altitude’ specifically refers to the distance of an object above mean sea level (AMSL) and is based on a local pressure setting. This pressure setting is referred to as the QNH, where NH stands for ‘nautical height’.
The term ‘height’ specifically refers to the distance of an object above ground level at a given point and is based on a local pressure setting. This pressure setting is referred to as the QFE, where FE stands for ‘field elevation.’
To calculate the QFE in millibars:
  Determine the landing elevation using a chart.
  Where one millibar of pressure equates to 28ft of altitude; divide the landing elevation by 28.
  The result is the difference between the QNH and the QFE. Find the local QNH, subtract the result of the previous calculation and the result is the QFE.
494(P)-NAV-01

## Slide 17: Altitudes, Heights and Flight Levels
A flight level measures altitude, but using a standard pressure setting.
Above the ‘transition altitude’ – a locally specified altitude at which aircraft should set ‘standard pressure’, altitudes are referred to by flight level.
By using a standard pressure setting in this way, aircraft are operating on a common reference, ensuring that local variations in pressure do not cause altitude conflicts and vertical separation can be maintained.
494(P)-NAV-01

## Slide 18: Navigation and Vertical Separation
Whilst modern aircraft and air traffic management platforms have a variety of systems available to ensure separation, such as TCAS, aircraft borne radars and surveillance systems, many basic principles are still used to ensure separation is maintained in the event that these systems failed.
The most common of these is the ‘hemispheric rule’ or ‘semi-circular rule’. The rule says that:
  When the magnetic track of an aircraft is between 0 and 179 degrees, the aircraft should fly at an odd flight level (190, 210, 230, 250).
  When the magnetic track of an aircraft is between 180 and 359 degrees, the aircraft should fly at an even flight level (180, 200, 220, 240).
Whilst in a tactical environment, it is not expected that a flight adhere to the hemispheric rule, aircraft transiting to or from tactical environments should consider doing so where possible.
494(P)-NAV-01

## Slide 19: Dead Reckoning/VFR Navigation
Usable Features
Starting and Finishing a ‘Leg’
494(P)-NAV-01

## Slide 20: Usable Features
Dead Reckoning navigation is one of the most useful skills in a pilot’s arsenal, particularly when flying tactically. Being able to orient oneself based on terrain features may aid in target location.
When undertaking navigation in this way, any easily distinguishable land feature that is not likely to change may be used. For example:
  Cities of distinctive shapes
  Roads, Rivers and Railways
  Physical landmarks, such as peaks of hills, geographical features or distinctive buildings.
494(P)-NAV-01

## Slide 21: Starting and Finishing a ‘leg’
A section of flight between two points performed using dead reckoning navigation is referred to as a ‘leg’.
When starting a leg, it is important to ensure that navigation starts either overhead the starting point, or overhead some known location so that the accuracy of the leg may be monitored.
Where possible, the distance between two points should be measured and a timer started when leaving the first point.
Given a constant ground speed, the time between two points may be calculated if the difference is known.
494(P)-NAV-01

## Slide 22: Starting and Finishing a ‘leg’
Whilst flying between the start and end of a leg, features that are crossed over should be referenced against other known landmarks in order to evaluate the accuracy of the flight. Corrections should be made as early as possible where deviations are detected.
When approaching the anticipated end of the leg, three distinct features should be used to evaluate whether or not the point reached is the desired point. For example:
  The time between legs is roughly accurate
  A distinctive landmark is visible in the expected place
  A road leads into the destination from the desired direction and can be seen visually.
494(P)-NAV-01